## Slide 1: Instruction Pipelining
Pushpendra Kumar Pateriya

## Slide 2: Performance
It is the time taken by the system to execute a program.
Performance affected by following parameters:
  Clock speed
  Type and number of instructions available
  Average time required to execute an instruction
  Memory access time
  Power dissipation in the system
  Number of I/O devices and types of I/O devices connected
  The data transfer capacity of the bus

## Slide 3: Important Fact
CPI: Cycles per instruction
IPC: Instructions per cycle
IPC = 1/CPI
CPU clock cycles = Number of instructions X Average clock cycles per instruction
CPU clock cycles
CPU execution time = CPU clock cycles X Clock cycle time
CPU execution time = CPU clock cycles / Clock rate
CPU execution time = Instruction Count X CPI X Clock Cycle Time
CPU execution time =
CPU execution time = Seconds / Program
Speedup = (Earlier execution time) / (Current execution time)

## Slide 4: Instruction Processing
Single Cycle | Multiple Cycle | Pipeline
Cycle time long enough for the longest instruction | Cycle time long enough for the longest stage | Cycle time long enough for the longest stage
Entire cycle acts as a single stage | Shorter stages waste time | Shorter stages waste time
Shorter instruction waste time | Shorter instructions can take fewer cycles | No additional benefit from shorter instructions
No overlap | No overlap | Overlap instruction execution

## Slide 5: 5 Stage Instruction Cycle
Instruction Fetch
Decode (Interpret) Instruction
Fetch Operands
Perform Operation
Store Result

## Slide 9: Pipeline Design and Issue

## Slide 10: Problems in Instruction Pipelining
Timing Variations
Data Hazards
Branching
Interrupts

## Slide 11: Pipeline Hazards
Structural Hazard
  Different instructions trying to access the same piece of H/W in the same segment of pipeline.
Data Hazard
  Instruction depends on the result of a prior instruction
    RAW (True Data Dependency/Flow Dependency)
    WAR (Antidependency)
    WAW (Output Dependency)
Control Hazard

## Slide 12: Berstein’s Conditions

## Slide 14: Handling Data Hazards
Forwarding: (Add special circuitry, which one forwards the desired value to the pipeline segment)
Code Re-Ordering
Stall Insertion: (n0-op instruction)

## Slide 15: Control Hazard
Can result from branch instructions
Types of control hazards:
  Jump to the branch target address if the instruction succeeds
  Execute the instruction after the branch instruction if the branch fails